## Slide 1
AA
ALLEN ALLISON
Chief Information Security Officer
Cybersecurity Executive | CISO
AA@allenallison.com · linkedin.com/in/allen-allison-ciso
FDA PREMARKET CYBERSECURITY GUIDANCE 2026
Executive Briefing · What Changed & What It Means For Your Organization
Issued February 3, 2026 · FDA CDRH & CBER · Docket FDA-2021-D-1158
CONFIDENTIAL · ALLEN ALLISON · CISO

## Slide 2
AGENDA
Topics Covered in This Briefing
02
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
01
What Changed
Key updates from the 2014 guidance and why FDA issued new guidance now
02
Scope & Applicability
Which devices and submissions are covered — including cyber devices under §524B
03
The SPDF Framework
Secure Product Development Framework — what FDA expects from manufacturers
04
Security Risk Management
Threat modeling, SBOM, cybersecurity risk assessment requirements
05
Transparency & Labeling
Cybersecurity Management Plans and labeling obligations
06
Action Items
What your organization needs to do now

## Slide 3
01
WHAT CHANGED
From 2014 Guidance to 2026 — A Decade of Evolution
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026

## Slide 4
WHAT CHANGED FROM 2014 TO 2026
Key Regulatory Shifts
04
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
🔐
Cybersecurity = Patient Safety
Explicitly embedded in the Quality Management System Regulation (QMSR). No longer a separate track — it's part of device safety by definition.
📋
SPDF Now Expected
The Secure Product Development Framework (SPDF) is the recommended approach to satisfy QMSR cybersecurity requirements across the total product lifecycle.
📦
SBOM Required
A complete Software Bill of Materials is required for all submissions — every proprietary, commercial, and open source component must be documented and assessed.
⚖️
Section 524B Codified
FDORA (2022) added §524B to the FD&C Act. Cyber devices must now legally comply with cybersecurity requirements — not just recommended practice.
🔍
Threat Modeling Mandated
Threat modeling must occur throughout the design process, not just at submission. Hospital networks should be assumed hostile by default.
📢
Transparency Obligations
Device labeling must disclose cybersecurity controls, known vulnerabilities, update procedures, and secure configuration guidance.

## Slide 5
SCOPE & APPLICABILITY
Which Devices and Submissions Are Covered
05
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
✅ APPLIES TO
→ All devices with software, firmware, or programmable logic
→ Premarket submissions: 510(k), PMA, De Novo, HDE, BLA, IND, IDE
→ Devices that DO NOT require premarket submission (510(k)-exempt)
→ Combination products with device constituent parts
→ "Cyber devices" as defined in §524B of the FD&C Act
→ Both CDRH and CBER regulated devices
⚡ CYBER DEVICE — §524B DEFINITION
A device qualifies as a "cyber device" when it meets ALL three criteria:
1
Includes software validated, installed, or authorized by the sponsor as a device or in a device
2
Has the ability to connect to the internet
3
Contains technological characteristics that could be vulnerable to cybersecurity threats
⚠ Failure to comply with §524B(b)(2) is a prohibited act under §301(q) of the FD&C Act.

## Slide 6
02
THE SPDF FRAMEWORK
Secure Product Development Framework — What FDA Expects
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026

## Slide 7
SECURE PRODUCT DEVELOPMENT FRAMEWORK (SPDF)
FDA's Recommended Approach to Satisfy QMSR Cybersecurity Requirements
07
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
🎯
Security Risk Management
Threat modeling, cybersecurity risk assessment, SBOM, vulnerability management across the TPLC
🏗
Security Architecture
Implementation of security controls: authentication, authorization, cryptography, confidentiality, updatability
🧪
Cybersecurity Testing
Penetration testing, fuzz testing, vulnerability scanning, static/dynamic analysis — documented and submitted
📋
Submission Documentation
Security risk management report, architecture views, testing results, SBOM — all required in premarket submissions
APPLIES ACROSS THE TOTAL PRODUCT LIFECYCLE (TPLC): Design → Development → Manufacturing → Distribution → Postmarket → Decommission

## Slide 8
SECURITY RISK MANAGEMENT
Threat Modeling · Risk Assessment · SBOM · Vulnerability Management
08
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
🎯 THREAT MODELING
→ Must be performed throughout the design process — not a one-time submission artifact
→ Assumes hospital networks are hostile (adversary controls network traffic)
→ Must capture risks from supply chain, manufacturing, deployment, interoperability, and decommission
→ Identifies security objectives, risks, vulnerabilities, and countermeasures
→ Results must be traceable to SBOM and cybersecurity risk assessment
📦 SOFTWARE BILL OF MATERIALS (SBOM)
→ Every software component — proprietary, OTS, and open source
→ Component version, support status, and known vulnerabilities
→ Vulnerabilities on CISA's Known Exploited Vulnerabilities (KEV) Catalog must be designed out
→ Traceability to security risk assessment required
⚠ CYBERSECURITY RISK ASSESSMENT
→ Non-probabilistic approach — focuses on exploitability, not frequency
→ Exploitability increases over the device lifecycle
→ Acceptance criteria must account for TPLC (not just day-0 risk)
→ CISA KEV catalog vulnerabilities = known exploited = design them out

## Slide 9
SECURITY ARCHITECTURE & TESTING
Required Controls and Verification Evidence for Premarket Submissions
09
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
FDA SECURITY OBJECTIVES — ALL DEVICES MUST ADDRESS:
Authenticity (incl. Integrity)
Authorization
Availability
Confidentiality
Secure & Timely Updatability
🔑 Authentication & Authorization
· Multi-factor authentication required
· Role-based access control
· Unique device identity
· Session management controls
· No hardcoded credentials
🔒 Cryptography & Integrity
· Encrypted communications (TLS 1.2+)
· Code signing for firmware/software
· Tamper detection mechanisms
· Secure boot where applicable
· Key management processes
🔄 Resilience & Updates
· Secure and authenticated update mechanism
· Ability to update in the field without downtime
· Audit logging and event detection
· Backup and recovery capabilities
· End-of-life planning documented
🧪 REQUIRED TESTING: Penetration testing · Fuzz testing · Static/dynamic analysis · Vulnerability scanning · Binary analysis — all results must be submitted

## Slide 10
TRANSPARENCY & CYBERSECURITY LABELING
What Manufacturers Must Disclose — and Why It's a Safety Requirement
10
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
📢 REQUIRED LABELING ELEMENTS
→ All cybersecurity controls implemented in the device
→ Known but unmitigated vulnerabilities and residual risks
→ All communication interfaces and network connections
→ Secure configuration instructions for deployment
→ Patch/update procedures and timelines
→ Instructions for end-of-life security management
→ How to detect and respond to cybersecurity incidents
📋 CYBERSECURITY MANAGEMENT PLAN (CMP)
→ How the manufacturer will monitor postmarket vulnerabilities
→ Coordinated vulnerability disclosure process (CVD)
→ Patch availability and deployment commitments
→ End-of-support notification to customers
→ Communication plan for security advisories
⚠ REGULATORY CONSEQUENCE
Failure to disclose adequate cybersecurity information may render a device MISBRANDED under §502(f) or §502(j) of the FD&C Act. For cyber devices, non-compliance with §524B(b)(2) is a prohibited act under §301(q).

## Slide 11
ACTION ITEMS FOR YOUR ORGANIZATION
What To Do Now — Prioritized by Urgency
11
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026
🔴
IMMEDIATE
Audit all current premarket submissions — do they address the 5 security objectives? · Assess whether your devices meet the "cyber device" definition under §524B · Map your current submission documentation against new SBOM requirements
🟡
SHORT-TERM (30–90 DAYS)
Integrate threat modeling into your design review process as a standing gate · Stand up a continuous SBOM process — not a point-in-time document · Audit third-party software components against CISA's KEV Catalog · Develop or update your Cybersecurity Management Plan
🟢
STRATEGIC (90–180 DAYS)
Implement a Secure Product Development Framework (SPDF) or validate existing processes against FDA expectations · Establish a Product Security Incident Response Team (PSIRT) with defined escalation paths · Update device labeling templates to include all required cybersecurity disclosures · Train quality, regulatory, and engineering teams on QMSR cybersecurity integration
📅 EFFECTIVE DATE: February 3, 2026 — Supersedes June 27, 2025 guidance. Questions: CyberMed@fda.hhs.gov · Docket: FDA-2021-D-1158

## Slide 12
AA
ALLEN ALLISON
Chief Information Security Officer
Cybersecurity Executive | CISO
AA@allenallison.com linkedin.com/in/allen-allison-ciso allenallison.com
Questions & Discussion
FDA Premarket Cybersecurity Guidance 2026
Docket FDA-2021-D-1158 · Issued February 3, 2026 Document number GUI00001825 · Contact: CyberMed@fda.hhs.gov
CONFIDENTIAL · ALLEN ALLISON · CISO · FDA PREMARKET CYBERSECURITY GUIDANCE 2026